## Slide 1: MT 3000-3(i) PowerFeeder

## Slide 2: MT 3000-3(i) Standard and Offset
Two machines - one concept
  MT 3000-3(i) Standard material feeder with short, rigid conveyor
  MT 3000-3(i) Offset material feeder with long, pivoting conveyor

## Slide 3: MT 3000-3(i) Standard
  Classic material feed process for large quantities of mix
  Uninterrupted supply of mix
  Paving process without pauses
  For large road construction projects
    Rehabilitation of major roads
    Paving large widths
    Large layer thicknesses

## Slide 4: MT 3000-3(i) Offset
  Uninterrupted, contact-free supply of mix
  Broad range of applications
    Classic material feed process
    Feeding from the side
    Material feed process for working “hot to hot”
    Feeding pavers in an InLine Pave train

## Slide 5: Highlights
  The new generation of material feeders
  Modern drive concept
  Redesigned receiving hopper
  Optimized conveying of mix
  Optimized belt heating
  ErgoPlus 3
  AutoSet Plus
  PaveDock Assistant
  New maintenance and service concept

## Slide 6: Modern drive concept

## Slide 7: Modern drive concept – MT 3000-3
High conveying capacity with quiet, economical operation
  Engine: Deutz TCD 2012
  Output:
    Nominal output: 142 kW at 2,000 rpm
    ECO Mode: 134 kW at 1,800 rpm
  Exhaust emissions standards:
    European exhaust emissions standard Stage 3a
    US standard EPA Tier 3
  Fuel tank: 450 litres

## Slide 8: Modern drive concept – MT 3000-3i
High conveying capacity with quiet, economical operation
  Engine: Deutz TCD 6.1
  Output:
    Nominal output: 160 kW at 2,000 rpm
    ECO Mode: 152 kW at 1,800 rpm
  Exhaust emissions standards:
    European exhaust emissions standard Stage V
    US standard EPA Tier 4f
  Fuel tank: 450 litres

## Slide 9: Modern drive concept
Controlled hydraulic oil cooler
  The controlled hydraulic oil cooler significantly reduces noise emissions
  Hydraulic engine with integrated speed sensor and electric proportional adjustment

## Slide 10: Modern drive concept
Electrical package with 230 V
  Hydraulically-driven three-phase AC generator
  Socket (earthed) plus two connections for light balloons
  Heating for the belt scraper

## Slide 11: Redesigned receiving hopper

## Slide 12: Redesigned receiving hopper
New receiving hopper geometry
  Highlighted hopper sides
  Raised hopper floor marked in colour
  Outer ends of push-roller marked in colour

## Slide 13: Optimized conveying of mix

## Slide 14: Optimized conveying of mix
Modified receiving area
  Rapid, loss-free receiving and conveying of a complete truckload
  Cylindrical augers with optimized auger protection
  Inlet area behind the deflection drum
  Inlet area sealed off to prevent contamination inside conveyor
  Option: conical augers homogenize the mix perfectly

## Slide 15: Optimized conveying of mix
Perfect belt running
  Improved belt guidance keeps the conveyor belt permanently centred
  Conveyor belt is centred even under difficult conditions of use such as transverse slopes
  Lateral buffer rollers stop the conveyor belt chafing on the frame
  No loss of material and reduced wear

## Slide 16: Optimized belt heating

## Slide 17: Optimized belt heating
New belt heating control
  Significantly reduces fuel consumption
  Reliably maintains mix at the correct temperature
  Reduces adherence of mix to the conveyor belt
  Allows the handling of critical mixes such as low-temperature asphalt

## Slide 18: ErgoPlus 3 operating concept

## Slide 19: ErgoPlus 3 operating concept
Convenient, ergonomic, safe and simple
  ErgoPlus 3 makes humans the focus
  Machine simple and intuitive to operate
  Ergonomic and safe workplace for the operator
  Full control of machine and project

## Slide 20: ErgoPlus 3 operator’s platform
Convenient, clear and comfortable
  Good all-round visibility
  Plenty of stowage space
  No edges to trip over
  Protection from wind and rain
  Swivelling operator’s seat
  Weather protection on the sides for greater comfort during operation

## Slide 21: ErgoPlus 3 operator’s console
Logical, practical and intuitive
  Functions in logical groups
  Touch and Work functions are executed directly without repeat confirmation
  Automatic background lighting
  Based on the ErgoPlus 3 operating system for pavers

## Slide 22: ErgoPlus 3 operator’s console – display
  Simple menu structure
  Optimized operating logic prevents faulty operation
  Various process situations displayed
  New, logical arrangement of symbols
  Reduced settings

## Slide 23: ErgoPlus 3 – joystick for Offset
Simple operation of the pivoting conveyor
  Raise/lower conveyor
  Rotate conveyor
  Speed of conveying process
  Conveying process, automatic mode
  Conveying process, manual mode
  Second joystick available as an option
  Can simply be detached and stowed

## Slide 24: AutoSet Plus

## Slide 25: AutoSet Plus
Repositioning functions
  For job sites involving frequent repositioning and for transport
  Conveying programs
  Conveying programs which are predefined and can be saved individually

## Slide 26: AutoSet Plus - repositioning functions
Can be repositioned quickly and easily
  In repositioning or transport position at the touch of a button:
    deflector
    pivoting conveyor boom
    material hopper
    hopper side
  Everything returned to the saved operating position at the touch of a button

## Slide 27: AutoSet Plus - conveying programs
Save simply and intuitively
  Predefined programs for low, moderate and high conveying capacity
  Conveying programs can be saved individually
  Saved parameters:
    settings for conveyors and augers
    belt heating
    distance from paver

## Slide 28: PaveDock Assistant

## Slide 29: PaveDock Assistant
Straightforward communication between material feeder operator and truck
  Two signal lights tell the truck driver:
    to drive off
    to stop
    to dump mix
  Makes material transfer safe, loss-free and efficient

## Slide 30: PaveDock Assistant – signal lights
Dock
Stop
Raise dump box
Lower dump box
Drive off
Material feeder moving

## Slide 31: PaveDock Assistant – signal lights
Material feed for the InLine Pave process
With Inline Pave mode activated, a symbol for the corresponding material is displayed as a function of the distance selected.
  Feeding surface course material – short distance control set
  Feeding binder material – long distance control set
Feed surface course material
Feed binder material

## Slide 32: New maintenance and service concept

## Slide 33: New maintenance and service concept
Quick and easy to maintain
  Maintenance access for the belt, electrical system and hydraulic filter on the operator's platform

## Slide 34: New maintenance and service concept
Quick and easy to maintain
  Relevant setting points are marked in colour
  Simplified settings on the belt and conveyor system
  Better sealing of the material hopper means less cleaning effort

## Slide 35: New maintenance and service concept
Specially designed for the MT 3000-3(i) Offset
Transfer hopper from the primary belt to the pivoting conveyor is especially easy to clean:
  good access
  extended step for a steady footing
  hopper is hinged
  machine can be cleaned in its operating position

## Slide 36: Use and transport

## Slide 37: In action
Feeding from the side
Classic material feed process
Feeding pavers in an InLine Pave train
Feeding Mini Class pavers

## Slide 38: Simple transport of the Offset
  The climbing angle of 15° makes it easier to get up onto low-loaders
  The receiving hopper can be raised and put down on the low-loader
  Optimized transport length

## Slide 39: Dimensions and weights
MT 3000-3(i) Standard
  Width: 3,000 mm
  Length: 8,950 mm
  Height: 3,100 mm
  Weight: 19,765 kg
MT 3000-3(i) Offset
  Width: 3,000 mm
  Length: 14,710 mm
  Height: 3,100 mm
  Weight: 24,285 kg

## Slide 40: MT 3000-3(i) Standard and Offset
  Engine capacity:
    MT 3000-3: 160 kW
    MT 3000-3i: 142 kW
  Exhaust emissions standards:
    MT 3000-3: Stage 3a; EPA Tier 3
    MT 3000-3i: Stage V; EPA Tier 4
  Pave speed 25 m/min
  Travel speed: 4.5 km/h
  Conveying capacity: 1,200 t/h
  Volume of transfer hopper: 15 t